## Slide 1: IETF Hackathon -IFIT & APN6
IETF 108
July 20-24, 2020
Online

## Slide 2: Hackathon Plan
Implemented a demo for IFIT and APN6 respectively, based on P4
Conducted some simulations of these demos, based on BMv2
  IFIT Documents:
    https://tools.ietf.org/id/draft-song-opsawg-ifit-framework-06.html
    https://tools.ietf.org/html/draft-ietf-ippm-ioam-data
    ​https://tools.ietf.org/html/draft-ietf-ippm-ioam-ipv6-options
    https://dl.acm.org/doi/abs/10.1145/3342280.3342292
  APN6 Documents:
    https://tools.ietf.org/html/draft-li-apn-problem-statement-usecases-00
    ​https://tools.ietf.org/html/draft-li-apn-framework-00
    ​https://tools.ietf.org/html/draft-li-6man-app-aware-ipv6-network-02
    ​https://tools.ietf.org/html/draft-zhang-apn-acceleration-usecase-00
    https://tools.ietf.org/html/draft-liu-apn-edge-usecase-00
  APN6 Community: https://github.com/APN-Community

## Slide 3: IFIT & APN6
Fine-grained closed-loop traffic control
In-situ telemetry for operators
Provide reliable, real-time and diverse types of data
Application-aware control
Based on service requirements

## Slide 4: IFIT Introduction
In-situ telemetry for operators.
  Encapsulate IOAM Options to indicate desired types of data.
  Transit Nodes can obtain indicated data under some set conditions
  2 modes of IOAM telemetry
Postcard
Passport

## Slide 5: APN6 Introduction
Application-aware traffic control.
  Make use of the IPv6 extensions header to convey the service requirements, in the form of APN6 options and optional Sub-TLV.
  Determine the SRv6 SID List based on the encapsulated options and Sub-TLV
  An Instance

## Slide 6: Implemented Functions
We’ve implemented the demo based on P4, and conducted some simulations based on BMv2.
Functions in Demo
  IFIT:
  The encapsulation of IOAM Options for specified flows
  Transit Nodes obtain specified data, support 4 types
  Both Postcard mode and Passport mode are implemented
  APN6:
  The encapsulation of APN6 Options and Serice-Para Sub-TLV, support 2 types of APN6 Options and 4 types of Sub-TLV
  The encapsulation of the SRv6 SID List according to IPv6 DA and APN6 options
  Basic SRv6 END SID processing

## Slide 7: Outcomes
Simulation Videos:
We’ve uploaded the simulation videos of IFIT and APN6 to the public cloud, you can get them through the following 2 links. We’ve confirmed that the resolution can support the clear view of terminals.
IFIT Simulation: https://1drv.ms/v/s!AlsZ1mjF7rg4ynhJhrrHXdvQaH5K?e=1GN5Lg
APN6 Simulation: https://1drv.ms/u/s!AlsZ1mjF7rg4ywU7nCHbniBHwr2h?e=ubZa1H
(You can set the resolution on the playback bar)

## Slide 8: Future Plan
Transplant the Demos to the Barefoot Tofino switch.
Deploy the simulation on CENI
CENI: An experiment infrastructure
Node City
100
G
Connection
Nanchang
Urumqi
Lhasa
Xining
Lanzhou
Yinchuan
Hohhot
Taiyuan
Xi'an
Chengdu
Kunming
Guiyang
Nanning
Haikou
Chongqing
Changsha
Wuhan
Zhengzhou
Beijing
Shenyang
Changchun
Harbin
Qiangdao
Dalian
Jinan
Tianjin
Nanjing
Hefei
Shanghai
Fuzhou
Xiamen
Shenzhen
Guangzhou
Zhuhai
Ningbo
Shijiazhuang
Hangzhou
Zhangjiakou
Suzhou
Xuchang
Characteristics:
For the next-generation networks, Cyberspace security, and Space Terrestrial Integrated Network
Contain OTN, SDN, and Programmable network
The NOS that support 400 cities, 1100 nodes

## Slide 9: Wrap Up
Team members:
Dr. Weihong Wu: wwh_bupt@foxmail.com or lara@bupt.edu.cn
Prof. Jiang Liu: liujiang@bupt.edu.cn